## Slide 1: Business Case Analysis
Issue: Should we add a 65º C Scenario?
02
Most food and beverage facilities will want higher temperatures than 20-45º C.
Added cost of heat pump to achieve these temperatures may yield few cost-effective scenarios.
Technology changes could lead to higher temperature outputs from Microsoft data centers.
Higher temperature scenario may better position Microsoft to find F&B customers.
May argue for Microsoft increasing future heat recovery from data centers.

## Slide 2
Food and Beverage Sector Opportunities
Beverages
Industrial Sector | Unit Operations | Temperature Range | 
 |  | Celsius | Fahrenheit
Food | Drying | 30-90 | 90-210
 | Washing | 60-90 | 150-210
 | Pasteurizing | 60-80 | 150-190
 | Boiling | 95-105 | 220-140
 | Sterilizing | 110-120 | 250-270
 | Heat Treatment | 40-60 | 110-150
Beverages | Washing | 60-80 | 150-190
 | Sterilizing | 60-90 | 150-210
 | Pasteurizing | 60-70 | 150-170
The Opportunity
The Opportunity

## Slide 3
Why 65: New Technologies Will Recover More Heat
AI needs will generate more heat at data centers.
  Chips use more electricity, producing more heat. More processing, transistors, and faster processing drive this.
  AI accelerator hardware – field programmable gate arrays (FGPAs), graphical processing units (GPUs) and neural processing units (NPUs) – use more electricity and generate more heat.
  AI chips generate high volumes of heat in small, concentrated area, so harder to cool.
Liquid and immersion cooling can recover temperatures of at least 65 degrees C.
01
Section Title
Notes: See https://www.datacenterknowledge.com/ai-data-centers/assessing-ai-s-impact-on-data-center-heating-and-cooling-needs. Also https://www.thefastmode.com/expert-opinion/40963-cooling-the-ai-revolution-how-thermal-management-is-reshaping-data-centers#:~:text=AI%20and%20HPC%20workloads%20generate,costly%20and%20disruptive%20infrastructure%20overhauls.

## Slide 4
Why 65: Data Shows it is Possible
Intel-Submer OCP 9/24 Presentation – 70 degrees C
Advanced Liquid Cooling Technologies 7/24 OCP Presentation – 55-65 C
DGA’s 2022 Intel analysis – included 65 C scenario
EcoDataCenter says cold plate – 57 degrees
Qarnot says liquid immersion – 80 degrees
01
Section Title

## Slide 5
Heat Pump Adds Costs
Heat pumps add capex and opex.
Capex includes heat pump and extra piping.
Opex includes electricity and maintenance costs.
Must also obtain permits.
01
Section Title

## Slide 6
65º May Help Microsoft
Higher temperature scenario could better position Microsoft to find F&B customers.
May argue for Microsoft examining how to increase future heat recovery from data centers.
01
Section Title